## Slide 1
Light Emitting Diodes
Outline
- Luminescence Spectra of Atoms
- LEDs
. p-n Junction
. Light Outcoupling
- Organic LEDs
- Quantum Dots in LEDs

## Slide 2
“Characterization of Organic Illumination Systems”
April 1, 1989, Hamburgen et al.
Electrode #1
Penetration
Electrode #2
Penetration
Thermocouple Probe
Device Under Test
Electrode Separation
Dimensions in inches |  |  |  | 
Subject | Electrode Orientation | Electrode Separation | Electrode #1 Penetration | Electrode #2 Penetration
Bok Choy | parallel | 0.5 | 0.5 | 0.5
Mandarin Orange | parallel | 0.38 | 0.38 | 0.38
Cornichon | axial | 0.5 | 0.5 | 0.5
Kosher Pickle | axial | 2.5 | 1.0 | 1.5
Dill Pickle | axial | 2.5 | 1.0 | 1.5
Electrode Position:

## Slide 3
p-n Junctions and LEDs
High energy electrons (n-type) fall into low energy holes (p-type)
p-type
n-type
Resistor
Not
Shown
Resistor
Power Source
LED

## Slide 4
p-n Junctions and LEDs
ENERGY
Small Gap
Large Gap
Yellow
Light
Emitted
Red
Light
Emitted

## Slide 5
ANODE
CATHODE
Homojunction p-n Light Emitting Diode
Eg
Forward Bias condition
n
p
EC
EV
INJECTED ELECTRONS
p-n Diode
n
p
“+”
“−”
ELECTRICITY IN  LIGHT OUT
INJECTED HOLES
Eg
Zero bias condition
n
p
EC
EV
NO CHARGE
INJECTED (NO LIGHT OUT)
PHOTON EMITTED
Diode Current
Saturation Current in
Reverse Bias
Boltzman Constant
Temperature
Voltage Across Diode
Forward
Current
CURRENT
VOLTAGE
VB
Leakage
Current
Avalanche
Current
Breakdown
Voltage
Reverse
Voltage

## Slide 6
Extraction Efficiency of Planar LEDs
critical angle of total internal reflection
Problem: Only small fraction of light can escape from semiconductor.
Above equation gives < 10% extraction efficiency for typical III-V.
Trapped
light ray
High-index
semiconductor
Escape
Cone

## Slide 7
Artificial Lighting consumes 8% of US energy and 22% of US electricity
The energy cost is estimated at $50B annually or $200 per capita
Image in the Public Domain

## Slide 8
INSTALLED EFFICIENCY FRACTION
Incandescent 5% 12%
Fluorescent 20% 62%
HID lamps 25% 26%
White LEDs 35% ----
Note: Electric Motor Efficiency is 85%~90%
All Images are in the Public Domain

## Slide 9
Chart: 

 | 47.619 | 31.6667 | 42.8571 | 22.1429 | 32.8571 | 32.8571 | 35.4167 | 54.1667 | 37.5 | 70.375 | 37.5 | 54.1667 | 22.1429 | 31.6667 | 54.1667 | 53.125 | 54.1667 | 67.3077 | 61.5385 | 18 | 13.8333 | 65
Luminescence Efficiency [lm/W]
Color Rendering Index
Survey of Lightbulb Technology Performance
(using data from bulbs.com)
INCANDESCENT
HALOGEN
COMPACT FLUORESCENT
QD VISION
NEXXUS 110V LED
CREE LR6 LED
OTHER LED TECHNOLOGIES
CREE LRP38 LED
Tradeoff EFFICIENCY for COLOR QUALITY

## Slide 10
OLED: The Green Display
TV and PC Account for 1% each of US Electricity Usage
Plasma
LCD
RPTV
Power
Usage
[W/in2]
0.35
0.30
0.14
<0.05
OLED
Plasma, LCD, RPTV power usage values from 2007 CNet report on commercial TV power consumption. OLED value projected from SID 2007 demo. US household power usage data from 2004 report by the Natural Resources Defense Council.

## Slide 11
MIT OpenCourseWare
http://ocw.mit.edu
6.007 Electromagnetic Energy: From Motors to Lasers
Spring 2011
For information about citing these materials or our Terms of Use, visit: http://ocw.mit.edu/terms.